## Slide 2
The traction force from the wheel is applied to the axle
Parallel to the ground at the contact patch
1
1 = Fout

## Slide 3
This force can be broken into 2 components
1 pointing directly at the front axle
1 pointing 90 degree’s from the first
Fout * cos(alpha-theta)
2
3
2 = Fout * sin (alpha-theta)
3 = Fout * cos (alpha-theta)

## Slide 4
The force pointing at the front axle can be relocated (along it’s line of action) to that axle
2 = Fout * sin (alpha-theta)
3b = Fout * cos (alpha-theta)
2
3b

## Slide 5
Both of these forces can then be broken into 2 components
1 parallel to the ground at the contact point.
1 perpendicular to the ground at the contact point.
(note the angle of the ground may be different at each wheel the forces on each axle should match the angle of the ground for the wheel attached to that axle)
2 = Fout * sin (alpha-theta)
3b = Fout * cos (alpha-theta)
4 = Fout * sin (alpha-theta)* cos(alpha – theta)
5 = Fout * sin (alpha-theta)* sin(alpha– theta)
6 = Fout * cos (alpha-theta) * cos(beta-theta)
7 = Fout * cos(alpha-theta) * sin(beta-theta)
4
5
6
7

## Slide 6
The forces into the ground are counteracted by an equal/opposite normal force
2 = Fout * sin (alpha-theta)
3b = Fout * cos (alpha-theta)
4 = Fout * sin (alpha-theta)* cos(alpha – theta)
5 = Fout * sin (alpha-theta)* sin(alpha– theta)
6 = Fout * cos (alpha-theta) * cos(beta-theta)
7 = Fout * cos(alpha-theta) * sin(beta-theta)
4
5
6
7
NOTE – forces cancel depending on magnitude/direction
Need to find a way to determine this mathematically
(negative vs positive)

## Slide 7
The forces into the ground are counteracted by an equal/opposite normal force
4
5
6
4 = Fout * sin (alpha-theta)* cos(alpha – theta)
5 = Fout * sin (alpha-theta)* sin(alpha– theta)
6 = Fout * cos (alpha-theta) * cos(beta-theta)

## Slide 8
Each axle also experiences a force due to the weight of the vehicle
(these forces should sum to the total weight – but may not always be equal)
4
5
6
7
8
4 = Fout * sin (alpha-theta)* cos(alpha – theta)
5 = Fout * sin (alpha-theta)* sin(alpha– theta)
6 = Fout * cos (alpha-theta) * cos(beta-theta)
7 = W1
8 = W2

## Slide 9
These forces can also be split into components
1 parallel to the ground
1 perpendicular to it
4 = Fout * sin (alpha-theta)* cos(alpha – theta)
5 = Fout * sin (alpha-theta)* sin(alpha– theta)
6 = Fout * cos (alpha-theta) * cos(beta-theta)
7 = W1
8 = W2
9 = W1 * cos(90-alpha)
10 = W1 * sin(90-alpha)
11 = W2 * cos(90-beta)
12 = W2 * sin(90-beta)
9
10
11
12
7
8

## Slide 10
These forces can also be split into components
1 parallel to the ground
1 perpendicular to it
9
10
11
12
4
5
6
4 = Fout * sin (alpha-theta)* cos(alpha – theta)
5 = Fout * sin (alpha-theta)* sin(alpha– theta)
6 = Fout * cos (alpha-theta) * cos(beta-theta)
9 = W1 * cos(90-alpha)
10 = W1 * sin(90-alpha)
11 = W2 * cos(90-beta)
12 = W2 * sin(90-beta)

## Slide 11
The forces at each axle can be combined to give 2 forces on each wheel
1 parallel to the ground at that wheel
1 perpendicular to the ground at that wheel

## Slide 12
Any remaining forces into the ground will again be cancelled by equal/opposite normal forces

## Slide 13
Any remaining forces into the ground will again be cancelled by equal/opposite normal forces

## Slide 14
The remaining forces can be broken into X and Y components

## Slide 15
These forces can be relocated to the CG of the vehicle
(but we will need to add a force couple which will be calculated by the ‘lever’ arms)

## Slide 16
We can now slide the object based on the remaining forces at the CG (a=f/m; v=v+a; p=p+v)
We can also rotate the object based on the total remaining moments/couples (w=m/j; o=o+w; a=a+o)